This is my current collection of computer programs. All programs
run on IBM PC compatibles. Most BASIC programs will also run on
the MAC, though I am not certain that the new BSAVE and BLOAD
features will work. (These features are minor.) Screen graphics
work on both MAC and IBM from .BAS files. The .PAS programs are
now compatible with TURBO PASCAL 4.0 onward (e.g.; TURBO PASCAL
6.0. Previous versions were in TURBO 3.0, and had to be supplied
as object code.) All code is my own, unless otherwise specified.
All code is copyrighted, but may be freely distributed for no
compensation, as long as the author's name and copyright
notifications are included. Also, any modifications made to the
code must be documented with the updater's name and date.

I take no responsibility for damages that may result from the use
of these programs in decision making. Indeed, I have empirical
cause to doubt the validity of all RASP programs: Predicted
ascent times are consistently low in my experience. I have found
this to be the case in my data and in the data of others. (Bob,
You may recall how many people on the net told you your HP
rocket's parachute delay was correct. Your rocket nosed over and
fell a good distance before the chute ejected.) The programs
written by me and supplied here have been checked and rechecked,
however. Digital trajectory calculations are consistent with
closed form calculations. Predicted thrust curves have been
compared by superimposition with actual thrust curves. Most of
these programs have been around in one form or another for a
number of years.

I take no responsibility at all for code written by others.

-Larry Curcio

                           DATCOM.PAS
Puts out USAF DATCOM drag coefficient estimate given a rocket
configuration and a speed.

                    DATCOMFL.PAS, RASPFL.BAS
DATCOMFL.BAS puts out a file containing USAF DATCOM Cd estimates
for each integral velocity from 0 M/sec to 250 M/sec. RASPFL.BAS
uses the Cd file and the thrust curve files (see below) to
produce digital vertical trajectory statistics. Air density is
depreciated from 0 to 10,000 meters in altitude. Program abends
if 250m/sec is exceeded (trans-sonic region). RASPFL.BAS will
also use a unique Cd or drag constant.


              SIMLAB.PAS, SIMLABXL.PAS, SLIDES.PAS
SIMLAB.PAS produces a unique drag coefficient and drag constant,
given a rocket configuration. It also produces vertical
trajectory statistics. The drag coefficient/constant is
consistent with the average velocity of each stage. Up to 4
stages may be handled. SIMLABXL uses the drag constant produced
by SIMLAB to produce digital, off-vertical trajectory statistics
and 4-color graphs. Up to 4 stages may be handled in each flight,
up to 9 flights may be graphed on the same screen. SIMLABXL also
saves trajectory graphs, which may later be viewed with
SLIDES.PAS. SIMLAB.PAS and SIMLABXL.PA S use a file called
ENGINES.SLB. SIMLABXL also uses thrust curve files (see below).
[SIMLABXL is being updated to use drag files like RASPFL.BAS.]

                          SIMLAB-F.BAS
Produces simulated thrust curves for black powder engines, given
the grain configuration. Uses black powder propellant parameters
and pressure, exhaust velocity relationships. SIMLAB-F graphs the
curves and saves them as files, which contain all input as
documentation. Simulated thrust curves may be used by RASPFL,
SIMLABXL. They may be re-graphed using GRAPHENG.BAS. SIMLAB-F can
be used with other propellants if parameters are available, as
long as grain configurations belong to the conic frustum family.
Pressure/ Ve relationships for new propellants must be summarized
in DRAWCURV.BAS. PACMAN and C-SLOT configurations are not
supported.

         MIKE DORFFLER'S COMPOSITE THRUST CURVE PROGRAMS
Public domain programs in BASIC that give simulated thrust curves
for specified propellants and grain configurations. No file is
saved, though the programs are easily modified. Ideal gas law
approximations are used for pressure/exhaust velocity
relationships.


                          DRAWCURV.BAS
Takes a brief X-Y file and does a spline interpolation. The
splined graph is displayed and the user is allowed to update the
X-Y file in standard text editors without interrupting the
program run. The area under the graph is displayed as a check. An
interpolated file may be saved to any desired number of
intervals, up to 2000. DRAWCURV.BAS is useful for capturing
thrust curves from illustrations. (For this purpose, the area
under the graph corresponds to the total impulse.) In addition,
the splined polynomial formulas may be saved in a file. SIMLAB-
F.BAS uses such a file to summarize P/Ve relationships.

                          GRAPHENG.BAS
This program graphs thrust curve files (real or simulated),
discarding the first two lines, which contain only comments. It
allows the user to re-scale the graph, and to save the graphic as
a BASIC BSAVE file. Many word processors and graphics processors
take BLOAD format. A program is provided to display the graphics
files: BLOAD.BAS.

                     BLOAD.BAS, REFLECT.BAS
BLOAD.BAS displays a BASIC BLOAD file. REFLECT.BAS displays a
BSAVE file and creates a mirror image on IBM machines. Mirror
images are useful for tee-shirt transfer ribbons.

                             FM.BAS
Does a straight Fehskens-Malewicki approximation for vertical
flight statistics given impulse, burning time, launch mass,
diameter, and Cd.

                           NEWTON.BAS
Does a digital Newton's method backward search. Useful for
finding Cd from altitude, or altitude from ascent time. Must be
used in conjunction with a RASP program of very fine thrust curve
interval precision.

                          BACKTRAK.BAS
Finds Cd, ascent time from measured altitude; finds altitude, Cd
from ascent time. Uses FM approximation and digital Newton's
method. This is a marriage of NEWTON.BAS and FM.BAS.



                             CPRESS.BAS
Transcribed from AMSPAM. Author: Martin Catt. Not guaranteed by
me. (especially after STABCALC!) Finds center of pressure given
therocket configuration.

                           TRACK3.BAS
Reduces data for the 3-observer elevation-only tracking method.
The method itself is described in Stine's _HANDBOOK_. Trackers
are arrayed in a straight line a distance, D apart. 

                       THRUST CURVE FILES

Actual thrust curves supplied in analog readings by Jack Kane of
the NAR, translated into digital form (each with several hundred
intervals):

REALA8.ENG, REALB4.ENG. REALB6.ENG, REALB8.ENG, REALC5.ENG,
REALC6.ENG, REALD12.ENG


Rigorously simulated curves to NAR standard impulses, and ESTES
standard burning times (each with 500 intervals):

NARA8.ENG, NARB4.ENG, NARB6.ENG, NARC6.ENG, NARD12.ENG


Splined curves from illustrations (each with several hundred
intervals:

AEROG40.ENG, AEROF44.ENG